##### DRAFT EAST AFRICAN STANDARD

Automotive Gasoline(Premium Motor Spirit) — Specification

EAST AFRICAN COMMUNITY

Copyright notice

This EAC document is copyright-protected by EAC. While the reproduction of this document by participants in the EAC standards development process is permitted without prior permission from EAC, neither this document nor any extract from it may be reproduced, stored or transmitted in any form for any other purpose without prior written permission from EAC.

Requests for permission to reproduce this document for the purpose of selling it should be addressed as shown below or to EAC’s member body in the country of the requester:

© East African Community 2023 — All rights reserved

East African Community

P.O. Box 1096,

Arusha

Tanzania

Tel: + 255 27 2162100

Fax: + 255 27 2162190

E-mail: eac@eachq.org

Web: www.eac-quality.net

Reproduction for sales purposes may be subject to royalty payments or a licensing agreement. Violators may be prosecuted.

Foreword

Development of the East African Standards has been necessitated by the need for harmonizing requirements governing quality of products and services in the East African Community. It is envisaged that through harmonized standardization, trade barriers that are encountered when goods and services are exchanged within the Community will be removed.

The Community has established an East African Standards Committee (EASC) mandated to develop and issue East African Standards (EAS). The Committee is composed of representatives of the National Standards Bodies in Partner States, together with the representatives from the public and private sector organizations in the community.

East African Standards are developed through Technical Committees that are representative of key stakeholders including government, academia, consumer groups, private sector and other interested parties. Draft East African Standards are circulated to stakeholders through the National Standards Bodies in the Partner States. The comments received are discussed and incorporated before finalization of standards, in accordance with the Principles and procedures for development of East African Standards.

East African Standards are subject to review, to keep pace with technological advances. Users of the East African Standards are therefore expected to ensure that they always have the latest versions of the standards they are implementing.

The committee responsible for this document is Technical Committee EASC/TC 068, Petroleum and petroleum products.

Attention is drawn to the possibility that some of the elements of this document may be subject of patent rights. EAC shall not be held responsible for identifying any or all such patent rights.

This second edition cancels and replaces the first edition (EAS 158:2019) which has been technically revised.

# Automotive Gasoline(Premium Motor Spirit) — Specification1	Scope

This Draft East African Standard specifies requirements, sampling and test methods for automotive gasoline (Premium Motor Spirit), also commonly known as petrol, for use in spark ignition engines.

The standard applies to PMS as manufactured, stored, transported and marketed.

# 2	Normative references

The following referenced documents referred to in the text in such a way that some or all of their content constitutes requirements of this document. For dated references, only the edition cited applies. For undated references, the latest edition of the referenced document (including any amendments) applies.

ASTM D86, Standard test method for distillation of petroleum products at atmospheric pressure

ASTM D130, Standard Test Method for Corrosiveness to Copper from Petroleum Products by Copper Strip Test

ASTM D323, Standard test method for vapour pressure of petroleum products (Reid Method)

ASTM D381, Standard Test Method for Gum Content in Fuels by Jet Evaporation

ASTM D525, Standard Test Method for Oxidation Stability of Gasoline (Induction Period Method)

ASTM D1298, Standard Test Method for Density, Relative Density, or API Gravity of Crude Petroleum and Liquid Petroleum Products by Hydrometer Method

ASTM D1319, Standard Test Method for Hydrocarbon Types in Liquid Petroleum Products by Fluorescent

Indicator Adsorption

ASTM D2622, Standard Test Method for Sulphur in Petroleum Products by Wavelength Dispersive X-ray Fluorescence Spectrometry

ASTM D2699, Standard Test Method for Research Octane Number of Spark-Ignition Engine Fuel

ASTM D2700, Standard Test Method for Motor Octane Number of Spark-Ignition Engine Fuel

ASTM D3227, Standard Test Method for (Thiol Mercaptan) Sulphur in Gasoline, Kerosene, Aviation Turbine, and Distillate Fuels (Potentiometric Method)

ASTM D3237, Standard Test Method for Lead in Gasoline by Atomic Absorption Spectroscopy

ASTM D4052, Standard Test Method for Density, Relative Density, and API Gravity of Liquids by Digital Density Meter

1

ASTM D 4294, Standard Test Method for Sulfur in Petroleum and Petroleum Products by Energy Dispersive X-ray Fluorescence Spectrometry

ASTM D4952, Standard Test Method for Qualitative Analysis for Active Sulphur Species in Fuels and Solvents (Doctor Test)

ASTM D5191, Standard Test Method for vapour pressure of petroleum products (Mini method)

ASTM D5443, Standard Test Method for Paraffin, Naphthene, and Aromatic Hydrocarbon Type Analysis in Petroleum Distillates Through 200°C by Multi-Dimensional Gas Chromatography

ASTM D5453, Standard Test Method for Determination of Total Sulfur in Light Hydrocarbons, Spark Ignition Engine Fuel, Diesel Engine Fuel, and Engine Oil by Ultraviolet Fluorescence

ASTM D5580, Standard Test Method for Determination of Benzene, Toluene, Ethylbenzene, p/m-Xylene, oXylene, C9 and Heavier Aromatics, and Total Aromatics in Finished Gasoline by Gas Chromatography

ASTM D5599, Standard Test Method for determination of oxygenates in gasoline by gas chromatography and oxygen selective flame ionization detection

EN 237, Liquid petroleum products — Petrol — Determination of low lead concentrations by atomic absorption spectrometry

EN 238, Liquid petroleum products — Petrol — Determination of the benzene content by infrared spectrometry

EN 1601, Liquid petroleum products — Unleaded petrol — Determination of organic oxygenate compounds and total oxygen content by gas chromatography (O-FID)

EN 12177, Liquid petroleum products — Unleaded Petrol — Determination of benzene content by gas chromatography

EN 13016-1, Liquid petroleum products — Vapour pressure — Part 1: Determination of air saturated vapour pressure (ASVP)

EN 13132, Liquid petroleum products — Unleaded petrol — Determination of organic oxygenate compounds and total organically bound oxygen content by gas chromatography using column switching

EN 24260, Petroleum products and hydrocarbons — Determination of Sulphur content — Wickbold combustion method

IP 30, Detection of mercaptans, hydrogen sulphide, elemental sulphur and peroxides — Doctor test method

IP 40, Petroleum products — Determination of oxidation stability of gasoline — Induction period method

IP 123, Petroleum products — Determination of distillation characteristics at atmospheric pressure

IP 154, Petroleum products — Corrosiveness to copper — Copper strip test

IP 336, Petroleum products — Determination of sulphur content — Energy-dispersive-X-ray fluorescence method

IP 352, Determination of the lead content of automotive gasoline — Energy-dispersive x-ray fluorescence spectrometry method

IP 428, Liquid petroleum products — Petrol — Determination of low lead concentrations by atomic absorption spectrometry

IP 429, Liquid petroleum products — Petrol — Determination of the benzene content by infrared spectrometry ISO 1998, Petroleum industry — Terminology (all parts)

ISO 2160, Petroleum products — Corrosiveness to copper — Copper strip test

ISO 3170, Petroleum liquids — Manual sampling

ISO 3171, Petroleum liquids — Automatic pipeline sampling

ISO 3405, Petroleum products — Determination of distillation characteristics at atmospheric pressure

ISO 3675, Crude petroleum and liquid petroleum products — Laboratory determination of density — Hydrometer method

ISO 4259, Petroleum products — Determination and application of precision data in relation to methods of test

ISO 5163, Petroleum products — Determination of knock characteristics of motor and aviation fuels — Motor method

ISO 5164, Petroleum products — Determination of knock characteristics of motor fuels — Research method

ISO 6246, Petroleum products — Gum content of light and middle distillate fuels — Jet evaporation method

ISO 7536, Gasoline — Determination of oxidation stability of gasoline — Induction period method

ISO 8754, Petroleum products — Determination of sulphur content — Energy-dispersive X-ray fluorescence spectrometry

ISO 20847, Petroleum products — Determination of sulphur content of automotive fuels — Energy-dispersive

X-ray fluorescence spectrometry

ASTM D 4176, Standard Test Method for Free Water and Particulate Contamination in Distillate Fuels (Visual Inspection Procedures)

# 3	Terms and definitions

For the purposes of this document, the following terms and definitions apply.

ISO and IEC maintain terminological databases for use in standardization at the following addresses:

—	ISO Online browsing platform: available at http://www.iso.org/obp

##### 3.1 additive

material added to PMS, usually in small amounts, to impart or enhance desirable properties or to suppress undesirable properties

3.2 marketable distinct, acceptable smell for safe handling

##### 3.3 marker

chemical substances introduced into automotive gasoline for identification, traceability and regulation without altering their properties.

3.4

dye

chemical added to fuel for visual identification

3.5

portable containers are freight containers designed for intermodal transportation that is; land, sea, or air. There are various dimensions and classifications for these containers, making them interchangeable and stackable for efficient global trade.

# 4	Requirements

## 4.1	General requirements

4.1.1 Automotive gasoline shall be a volatile, flammable blend of hydrocarbons derived from petroleum refining.

4.1.2 Automotive gasoline shall possess a characteristic marketable odour

Automotive gasoline shall have;

a)	a marketable odour, and

b)	an appearance that is clear, bright and free from suspended particles on visual inspection.

## 4.2	Specific requirements

4.2.1	 Automotive gasoline shall comply with the requirements specified in Table 1 when tested in accordance with the test methods prescribed therein.

Table 1 — Specific requirements for automotive gasoline (premium motor spirit)

| S/No. | Property |  | Requirement |  | Test method |
| --- | --- | --- | --- | --- | --- |
|  |  | Min. |  | Max. |  |  |
|  | Appearance | Clear and bright free of visible particulate matter |  | ASTM D4176 |
|  | Research octane number (RON) |  | 93 |  | – | ISO 5164 ASTM D2699 |
|  | Motor octane number (MON) |  | 83 |  | – | ISO 5163 ASTM D2700 |
|  | Lead content, ppm |  | – |  | 5 | EN 237 ASTM D3237 IP 428 IP 352 |
|  | Benzene content, % v/v |  | – |  | 1.0 | EN 238 IP 429 EN 12177 ASTM D4420 |
|  | Total aromatics, % v/v |  | – |  | 42 | ASTM D1319 ASTM D5580 ASTM D5443 |
|  | Density (at 20 ºC), kg/m3 |  | 716 |  | 771 | ISO 3675 ASTM D4052 ASTM D1298 |
|  | Density (at 15 ºC), kg/m3 |  | 720 |  | 775 |  |
|  | Sulphur content, ppm |  | – |  | 10 | EN 24260 ISO 8754 ASTM D 4294 ASTM D 5453 |
|  | Manganese, ppm |  | – |  | 2.0 | ASTM D2622/IP 336 ISO 20847 ASTM D3831 ASTM D7111 |
|  | Oxidation stability, min. |  | 360 |  | – | ISO 7536/IP 40 ASTM D 525 |
|  | Existent gum content (solvent washed), mg/100 ml | – | 5 | ISO 6246 ASTM D381 |
|  | Copper strip corrosion (3 h at 50 °C), rating | – | No.1 strip | ISO 2160/IP 154 ASTM D130 |
|  | Mercaptan sulphur, %, m/m | – | 0.001 | ASTM D3227 |
|  | Oxygenates, % v/v |  | Nil | Nil | EN 1601 EN 13132 ASTM D5599 |
|  | RVP at 37.8 ºC, kPa |  | – | 65 | ASTM D323 ASTM D5191 EN 13016-1 |
|  | FVI b) |  | – | 93 | See table footnote b) |
|  | Distillation a) Temperature, °C for: • Initial boiling point |  | To be reported | ASTM D86 IP 123 |
|  | • 10 % volume evaporated | fraction | – | 71 |  |
|  | • 50 % volume evaporated | fraction | 77 | 115 |  |
|  | • 90 % volume evaporated | fraction | – | 180 |  |
|  | • Final boiling point, °C | – | 210 |  |
|  | b) Residue, % volume fraction | – | 2.0 |  |
|  | c) Evaporated to 70 °C (E70), % volume fraction | To be reported |  |
|  | Doctor test a | To be reported | ASTM D4952 IP 30 |
|  | Colour | Red | Visual inspection |
| If negative, no need to carry out Mercaptan sulphur test. The flexible volatility index (FVI) is an additional parameter which characterizes the volatility properties of petrol, and is calculated using the formula FVI = RVP + 0.7 E70 where RVP is the Reid vapour pressure, in kilopascals; and E70 is the percentage volume fraction of petrol, evaporated to 70 °C. |

#### 5 Dyes and markers

5.1 	The use of dyes and markers is allowed.

#### 5.2 The dye and markers content shall be reported and shall not alter any parameters of Automotive gasoline out of the specified range as indicated under Table 1. 6 Additives

In order to improve the fuel performance, the use of additives is allowed. Fuel additives without known harmful side effects are recommended in the appropriate amount to avoid deterioration of driveability and emissions control durability.

#### 7 Precision and dispute

7.1 All test methods referred to in this East African Standard include a precision statement. In cases of dispute, the procedures for resolving the dispute and interpretation of the results based on test method precision, described in ISO 4259, ASTM D 3244 and IP 377 shall be used.

7.2 	In cases of dispute:

- concerning sulphur, ISO 20847 is unsuitable as an arbitration method;

- concerning benzene content, EN 12177 shall be used;

- concerning oxygen and oxygenates content, EN 1601 shall be used; and

- concerning density, ISO 3675 shall be used.

#### 8 Packing and marking

##### 8.1 Packing

8.1.1 The condition of the containers, rail tankers and road tank vehicles shall be such as not to be detrimental to the quality of the fuel during normal transportation and storage.

8.1.2 The containers shall be acceptably sealed or leak proof, clean, and free from materials soluble in gasoline.

##### 8.2 Labelling

8.2.1 The following information shall appear in legible and indelible marked on the portable container, or on a label affixed to the portable  container:

- the supplier’s name or brand name or trade mark; and receiver’s name;

- the words, “UNLEADED PETROL” or “UNLEADED GASOLINE”, or “UNLEADED MOGAS”;

c) the batch number;

- the quantity in litres or metric tonnes;

- the words ”FLAMMABLE MATERIALS”; and

- the warning, “DANGER PETROL” or “DANGER UNLEADED GASOLINE”, or “DANGER UNLEADED MOGAS”

g. country of origin

8.2.2 For bulk transportation the above information shall be in the documentation accompanying the product and the respective container shall be marked with;

a. the words “FLAMMABLE MATERIAL”; and

b)	the warning “dangerous goods

8.2.3 Stickers shall be used in labelling in case of vehicles, which have compartments and transport more than one type of fuel.

8.2.4 Dispensing pumps used for delivering the fuel shall be clearly labelled with the wording ‘‘UNLEADED PMS/GASOLINE/PETROL’’, and the measurement dimensions of such shall be in accordance with the requirements of the relevant weights and measures regulations for each member state.

# 7	Sampling

Sampling shall be done in accordance with ASTM D4057 or ASTM D4177.

Bibliography

[1]	EAS 158:2019, automotive gasoline (premium motor spirit) — Specification